## Slide 1
Building
Blocks
W
W
,
hat is
oT
Notes: The third section of introduction to WoT is Building Blocks. In this video, we will explain each building block, WoT Thing description, Wot Discovery, WoT Binding templates, and WoT Scripting API.

## Slide 2: What are Building Blocks?
Notes: Let’s start with building blocks in general. What are building blocks?

## Slide 3
WoT Thing Description
Discovery
Bindings
Scripting API
Abstract WoT Architecture
Notes: Building blocks allow the implementation of systems that conform with the abstract WoT Architecture.

## Slide 4
Interaction Affordances
Security Metadata
Protocol Bindings
General Metadata
Data Schemas
WoT Thing Description
Thing
TD Directory
Private Security Data
Behavior
Scripting API
Consumer
Protocol Bindings
Notes: Let's look closer to the WoT building blocks.
It is an abstraction of the relationship between the building blocks and the main architectural aspects of a Thing.
A Thing always has a TD.
TD is a key building block that provides metadata describing a Thing and its network interface.
This TD can be shared directly by the Thing or through TD Directory
TDs can be restricted by the profiles for easier implementation
Things and consumers can be programmed with the scripting API.
The WoT Scripting API is optional, and the Binding Templates are informative.

## Slide 6
WoT Thing Description
Notes: After this overview let’s start with WoT Thing description.
All TDs can be represented in JSON-LD and can be processed just as a normal JSON.
And TD defines an information model according to a semantic vocabulary and a serialized representation of JSON. It is the key building block that provides human and machine-readable metadata describing the capabilities of a Thing and its network interfaces.

## Slide 7
WoT Thing Description
Notes: After this overview let’s start with WoT Thing description.
All TDs can be represented in JSON-LD and can be processed just as a normal JSON.
And TD defines an information model according to a semantic vocabulary and a serialized representation of JSON. It is the key building block that provides human and machine-readable metadata describing the capabilities of a Thing and its network interfaces.

## Slide 8
WoT Thing Description
JSON
Notes: After this overview let’s start with WoT Thing description.
All TDs can be represented in JSON-LD and can be processed just as a normal JSON.
And TD defines an information model according to a semantic vocabulary and a serialized representation of JSON. It is the key building block that provides human and machine-readable metadata describing the capabilities of a Thing and its network interfaces.

## Slide 9
WoT Thing Description
JSON
Notes: After this overview let’s start with WoT Thing description.
All TDs can be represented in JSON-LD and can be processed just as a normal JSON.
And TD defines an information model according to a semantic vocabulary and a serialized representation of JSON. It is the key building block that provides human and machine-readable metadata describing the capabilities of a Thing and its network interfaces.

## Slide 10
z
WoT Thing Description
Semantic Vocabulary
Serialized representation
JSON
Notes: After this overview let’s start with WoT Thing description.
All TDs can be represented in JSON-LD and can be processed just as a normal JSON.
And TD defines an information model according to a semantic vocabulary and a serialized representation of JSON. It is the key building block that provides human and machine-readable metadata describing the capabilities of a Thing and its network interfaces.

## Slide 11
z
WoT Thing Description
JSON
Notes: After this overview let’s start with WoT Thing description.
All TDs can be represented in JSON-LD and can be processed just as a normal JSON.
And TD defines an information model according to a semantic vocabulary and a serialized representation of JSON. It is the key building block that provides human and machine-readable metadata describing the capabilities of a Thing and its network interfaces.

## Slide 12
z
WoT Thing Description
Notes: After this overview let’s start with WoT Thing description.
All TDs can be represented in JSON-LD and can be processed just as a normal JSON.
And TD defines an information model according to a semantic vocabulary and a serialized representation of JSON. It is the key building block that provides human and machine-readable metadata describing the capabilities of a Thing and its network interfaces.

## Slide 13
Notes: After this overview let’s start with WoT Thing description.
All TDs can be represented in JSON-LD and can be processed just as a normal JSON.
And TD defines an information model according to a semantic vocabulary and a serialized representation of JSON. It is the key building block that provides human and machine-readable metadata describing the capabilities of a Thing and its network interfaces.

## Slide 14
General Metadata
Notes: TD describes Thing instances with general metadata such as name, ID, and description. In addition to that, TDs can also contain Interaction Affordance metadata and Protocol bindings.

## Slide 15
Title
ID
Description
Notes: TD describes Thing instances with general metadata such as name, ID, and description. In addition to that, TDs can also contain Interaction Affordance metadata and Protocol bindings.

## Slide 16
Interaction Affordance
Protocol Bindings
Notes: TD describes Thing instances with general metadata such as name, ID, and description. In addition to that, TDs can also contain Interaction Affordance metadata and Protocol bindings.

## Slide 17
Robot
Robot
Notes: The WoT TD building block enhances interoperability. The goal is to enable the communication within the machines.

## Slide 18
Robot
Controller
Notes: The WoT TD building block enhances interoperability. The goal is to enable communication within the machines or controllers.

## Slide 19
Notes: Typically, a programmer can read the robot's TD and program the controller accordingly to automate processes.

## Slide 20
Notes: Typically, a programmer can read the robot's TD and program the controller accordingly to automate processes.

## Slide 21
Notes: Typically, a programmer can read the robot's TD and program the controller accordingly to automate processes.

## Slide 22
Notes: Typically, a programmer can read the robot's TD and program the controller accordingly to automate processes.

## Slide 23
Robot
Controller
Request
Notes: Controller controls the robot by sending requests.

## Slide 24
Robot
Controller
Request
Notes: Controller controls the robot by sending requests.

## Slide 25
Robot
Controller
Request
Notes: Controller controls the robot by sending requests.

## Slide 26
z
WoT
Thing Description
WoT
Discovery
Notes: The next building blocks that we will introduce is WoT Discovery.

## Slide 27
Notes: WoT Thing Descriptions must be known or accessible to other systems and devices.

## Slide 28
Known
Accessible
Notes: WoT Thing Descriptions must be known or accessible to other systems and devices.

## Slide 29
WoT
Discovery
Notes: WoT Discovery building block accomplishes this by defining mechanisms for distributing and accessing WoT Thing Description over the network.

## Slide 30
Local Area Network
Notes: These mechanisms are used to simplify access to Things and services and support their integration. They are not limited to a local area network but they also support remote discovery.

## Slide 31
Notes: These mechanisms are used for simplifying access to Things and services and support their integration. They are not limited to a local area networks but they also support remote discovery.

## Slide 32
2
Notes: To achieve these functionalities, WoT Discovery uses a two-stage process. In the first stage, an introduction is made with one of the several first-contact mechanisms such as QR codes, mDNS, and DIDs. The second stage is the exploration phase where TDs are made available in TD directories so that they can be managed and searched.

## Slide 33
Stage Process
2
Notes: To achieve these functionalities, WoT Discovery uses a two-stage process.

## Slide 34
First Stage: Introduction
QR Codes
mDNS
And more
DIDs
Second Stage: Exploration
Notes: In the first stage, an introduction is made with one of the several first-contact mechanisms such as QR codes, mDNS, and DIDs.

## Slide 35
First Stage: Introduction
QR Codes
mDNS
And more
DIDs
Second Stage: Exploration
Notes: After the introduction, WoT Discovery defines a set of second-stage "exploration" mechanisms that provide actual access to metadata.
This can be done in 2 ways: a single TD can be retrieved or a link for TD directories becomes available.

## Slide 36
First Stage: Introduction
QR Codes
mDNS
And more
DIDs
Second Stage: Exploration
Notes: After the introduction, WoT Discovery defines a set of second-stage "exploration" mechanisms that provide actual access to metadata.
This can be done in 2 ways: a single TD can be retrieved or a link for TD directories becomes available.

## Slide 37
First Stage: Introduction
QR Codes
mDNS
And more
DIDs
Second Stage: Exploration
Notes: After the introduction, WoT Discovery defines a set of second-stage "exploration" mechanisms that provide actual access to metadata.
This can be done in 2 ways: a single TD can be retrieved or a link for TD directories becomes available.

## Slide 38
Notes: After the introduction, WoT Discovery defines a set of second-stage "exploration" mechanisms that provide actual access to metadata.
This can be done in 2 ways: a single TD can be retrieved or a link for TD directories becomes available.

## Slide 39
Notes: It is a database with a REST API to access TDs.

## Slide 40
TD
Directory
Register
Update
Retrieve
Search
Notes: Thing Description Directory service provides mechanisms to register, and retrieve WoT metadata and TDs after authentication and authorization.

## Slide 41
Introduction
Exploration
Direct
DNS-based Service Discovery
CoRE link Format
Well-known URIs
TD Server
TD
Directory
Notes: Thus we can summarize the Discovery mechanism like this.

## Slide 42
z
WoT
Thing Description
WoT
Discovery
WoT Binding
Templates
Notes: The third building block is WoT Binding Templates

## Slide 43
IoT
Notes: The IoT uses a variety of protocols for accessing devices because no single protocol is enough to cover the different use cases and requirements. The challenge of the WoT is to enable interactions of a variety of different IoT platforms.

## Slide 44
IoT
MQTT
HTTP
CoAP
…
Notes: The IoT uses a variety of protocols for accessing devices because no single protocol is enough to cover the different use cases and requirements. The challenge of the WoT is to enable interactions of a variety of different IoT platforms.

## Slide 45
WoT Binding
Templates
Matter
OCF (CBOR, CoAP, DTLS)
oneM2M (JSON, MQTT, TLS)
Cloud Providers (AWS, Azure…)
Commercial products
JSON
CBOR
XML
….
HTTP
MQTT
CoAP
Modbus
BACnet
….
IoT
Platform/
Framework
Protocol
and
Media Type
Notes: The Binding Templates address an application client to use the TD so that they can extract metadata of the protocols such as HTTP and MQTT etc., payload formats such as JSON and CBOR, etc. and their usage in an IoT framework context such as ECHONET and OPC.

## Slide 46
WoT Binding
Templates
Notes: In general, Binding Templates provides a collection of blueprints that give guidance on how to interact with different Things that use different transport protocols, and content types or that are different IoT platforms or standards that use certain combinations of transport protocols and content types.

## Slide 47
z
WoT
Thing Description
WoT
Discovery
WoT Binding
Templates
WoT Profile
Notes: Now we will introduce the profile.

## Slide 48
Notes: By nature, TD is flexible and able to describe anything without any limitations.

## Slide 49
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 50
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 51
Connect
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 52
Connect
Implementation
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 53
Connect
Implementation
Reduced implementation effort
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 54
Connect
Configurations
Network Protocol:
Security:
Data Structure:
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 55
Connect
Configurations
Network Protocol:
Security:
Data Structure:
HTTP
MQTT
CoAP
Notes: and while implementing a thing profile makes it way easier with providing guidance. For instance, developers don’t have to think about which protocols to choose.

## Slide 56
Connect
Security Key:
Configurations
IP Address:
***********
192.168. 0.1
A Specific Profile
Notes: Thus, in those cases, Profile limits the capabilities of the TDs which enables out of box interoperability among things and devices. And make it possible to communicate with only minor configuration operations such as entering a key or IP address.

## Slide 57
Connect
Notes: Thus, in those cases, Profile limits the capabilities of the TDs which enables out of box interoperability among things and devices. And make it possible to communicate with only minor configuration operations such as entering a key or IP address.

## Slide 58
Key:
IP Address:
***********
192.168. 0.1
Configurations
Notes: Thus, in those cases, Profile limits the capabilities of the TDs which enables out of box interoperability among things and devices. And make it possible to communicate with only minor configuration operations such as entering key or IP address.

## Slide 59
Key:
IP Address:
***********
192.168. 0.1
Configurations
Notes: Thus, in those cases, Profile limits the capabilities of the TDs which enables out of box interoperability among things and devices. And make it possible to communicate with only minor configuration operations such as entering key or IP address.

## Slide 60
z
WoT
Thing Description
WoT
Discovery
WoT Binding
Templates
WoT Profile
WoT Scripting API
Notes: Lastly, we will introduce WoT Scripting API, which is an optional building block of W3C WoT. It makes it easier to develop IoT applications by providing an ECMA Script-based API similar to the Web browser APIs.

## Slide 61
IoT applications
Notes: It makes it easier to develop IoT applications by providing an ECMAScript-based API similar to the Web browser APIs.

## Slide 62
Notes: It makes it easier to develop IoT applications by providing an ECMAScript-based API similar to the Web browser APIs.

## Slide 63
Scripting runtime system
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 64
Scripting runtime system
WoT runtime
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 65
WoT runtime
Scripting runtime system
WoT Scripting API
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 66
WoT runtime
Scripting runtime system
WoT Scripting API
Portable application
scripts
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 67
WoT runtime
Portable application
scripts
Behavior of
Things,
Consumer,
Intermediaries.
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 68
WoT runtime
setInterval(async ()=>){
const tempReading = await .readProperty("temperature")
const tempVal = await tempReading.value();
if(tempVal < 25){
await .invokeAction("increaseTemperature")
}
}
Protocol in TD: HTTP
httpThing
httpThing
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 69
WoT runtime
setInterval(async ()=>){
const tempReading = await .readProperty("temperature")
const tempVal = await tempReading.value();
if(tempVal < 25){
await .invokeAction("increaseTemperature")
}
}
Protocol in TD: Modbus
modbusThing
modbusThing
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 70
WoT runtime
setInterval(async ()=>){
const tempReading = await thing.readProperty(“temperature”)
const tempVal = await tempReading.value();
if(tempVal < 25){
await thing.invokeAction(“increaseTemperature”)
}
}
Protocol Option:
HTTP
Modbus
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 71
WoT runtime
setInterval(async ()=>){
const tempReading = await thing.readProperty(“temperature”)
const tempVal = await tempReading.value();
if(tempVal < 25){
await thing.invokeAction(“increaseTemperature”)
}
}
Protocol Option:
HTTP
Modbus
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 72
Application Logic does not Change!
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 73
Productivity
Integration cost
Notes: To summarize, WoT enables implementing device logic by reusable scripts executed in a runtime system for IoT applications which aims to improve productivity and reduce integration costs.

## Slide 74
NEXT VIDEO
Architecture
Patterns
Building
Blocks
Thing
Description
Notes: Next video we will explain the Thing Description.

## Slide 75
NEXT VIDEO
Architecture
Patterns
Building
Blocks
Thing
Description
Notes: Next video we will explain the Thing Description.