## Slide 1
Building
Blocks
W
W
,
hat is
oT
Notes: In this video, we give a short introduction to each building block of the Web of Things — Thing Description, Binding Templates, Discovery, Scripting API and Profiles. In separate later videos, we will explore each individual building block in more detail.

## Slide 2: What are WoT Building Blocks?
Notes: Building blocks allow the implementation of systems that conform with the abstract WoT Architecture. Let's take a closer look at the WoT building blocks.

## Slide 3
z
WoT
Thing Description
WoT
Discovery
WoT Binding
Templates
WoT Profile
WoT Scripting API
Notes: A Thing always has a TD, a Thing Description. It is a key building block that provides metadata describing a Thing and its network interface. This TD can be shared directly by the Thing or through the TD Directory — which is what we call Discovery. Things and consumers can be programmed with the Scripting API.

## Slide 4
WoT Thing Description
Notes: Let’s begin with the Thing Description, or TD — a key component of WoT.

## Slide 5
z
WoT
Thing Description
Notes: Let’s begin with the Thing Description, or TD — a key component of WoT.

## Slide 6
z
WoT Thing Description
Semantic vocabulary
Serialized representation
JSON
Notes: All TDs can be processed just like normal JSON documents. Essentially, a TD defines an information model using a semantic vocabulary and a serialized JSON representation. It provides both human- and machine-readable metadata describing the capabilities of a Thing.

## Slide 7
General Metadata
Notes: A TD describes a Thing instance with general metadata such as name, ID, and description. It can also contain Interaction Affordance metadata and Protocol Bindings (such as Modbus and HTTP), as well as both public and local IP addresses.

## Slide 8
Title
ID
Description
Interaction Affordances
Protocol Bindings
Notes: A TD describes a Thing instance with general metadata such as name, ID, and description. It can also contain Interaction Affordance metadata and Protocol Bindings (such as Modbus and HTTP), as well as both public and local IP addresses.

## Slide 9
z
WoT
Thing Description
WoT Binding
Templates
Notes: The second building block is WoT Binding Templates.

## Slide 10
IoT
MQTT
HTTP
CoAP
…
Notes: The IoT uses a wide variety of protocols to access devices because no single protocol can cover all use cases and requirements. One of the main challenges of the WoT is enabling interactions across this wide variety of platforms.

## Slide 11
WoT Binding
Templates
Matter
OCF (CBOR, CoAP, DTLS)
oneM2M (JSON, MQTT, TLS)
Cloud Providers (AWS, Azure…)
Commercial products
JSON
CBOR
XML
….
HTTP
MQTT
CoAP
Modbus
BACnet
….
IoT
Platform/
Framework
Protocol
and
Media Type
Notes: Binding Templates guide application clients on how to use a TD to extract protocol-specific metadata — for example, how to communicate using HTTP or Modbus. Essentially, they are blueprints for interacting with Things that use different transport protocols and content types.

## Slide 12
Example: Thing Description
Notes: Here is an example of a TD. This is the JSON serialization of a temperature controller. It tells the consumer to send a Modbus request to read the temperature in the local network. The Thing can also be proxied by a gateway where an HTTP request will be sent instead of a Modbus request.

## Slide 13
Example: Thing Description
Notes: Here is an example of a TD. This is the JSON serialization of a temperature controller. It tells the consumer to send a Modbus request to read the temperature in the local network. The Thing can also be proxied by a gateway where an HTTP request will be sent instead of a Modbus request.

## Slide 14
Thermostat
Robot
Notes: The WoT TD building block enhances interoperability. The goal is to enable communication within the machines or controllers.

## Slide 15
Thermostat
Controller
Notes: The WoT TD building block enhances interoperability. The goal is to enable communication within the machines or controllers.

## Slide 16
Notes: Typically, a programmer can read the robot's TD and program the controller accordingly.

## Slide 17
Notes: Typically, a programmer can read the robot's TD and program the controller accordingly.

## Slide 18
Notes: Typically, a programmer can read the robot's TD and program the controller accordingly.

## Slide 19
Controller
Notes: Typically, a programmer can read the robot's TD and program the controller accordingly.

## Slide 20
Controller
Notes: Typically, a programmer can read the robot's TD and program the controller accordingly.

## Slide 21
Controller
Notes: //new slide
Code flows into the controller

## Slide 22
Thermostat
Controller
Request
Notes: Controller then sends a request to the device from our example to change the temperature.

## Slide 23
Thermostat
Controller
Request
Notes: Controller then sends a request to the device from our example to change the temperature.

## Slide 24
Thermostat
Controller
Request
Notes: Controller then sends a request to the device from our example to change the temperature.

## Slide 25
WoT Binding
Templates
Notes: In general, Binding Templates provides a collection of blueprints that give guidance on how to interact with different Things that use different transport protocols, and content types or that are different IoT platforms or standards that use certain combinations of transport protocols and content types.

## Slide 26
z
WoT
Thing Description
WoT
Discovery
WoT Binding
Templates
Notes: The next building block is WoT Discovery.

## Slide 27
z
WoT
Thing Description
WoT
Discovery
Notes: The next building block is WoT Discovery.

## Slide 28
Notes: WoT Thing Descriptions must be known or accessible to other systems and devices.

## Slide 29
Known
Accessible
Notes: WoT Thing Descriptions must be known or accessible to other systems and devices.

## Slide 30
WoT
Discovery
Notes: WoT Discovery accomplishes this by defining mechanisms for distributing and accessing WoT TD over the network.

## Slide 31
Local Area Network
Notes: These mechanisms simplify access to Things and services and support their integration. They are not limited to a local area network - they also support remote discovery.

## Slide 32
Local Area Network
Notes: These could be mechanisms in local networks.
//put td in these devices
//then td from these devices is shown

## Slide 33
Notes: These mechanisms are used for simplifying access to Things and services and support their integration. They are not limited to a local area networks but they also support remote discovery.

## Slide 34
2
Notes: To achieve these functionalities, WoT Discovery uses a two-stage process. In the first stage, an introduction is made with one of the several first-contact mechanisms such as QR codes, mDNS, and DIDs. The second stage is the exploration phase where TDs are made available in TD directories so that they can be managed and searched.

## Slide 35
Stage Process
2
Notes: To achieve these functionalities, WoT Discovery uses a two-stage process.

## Slide 36
First Stage: Introduction
QR Codes
mDNS
And more
DIDs
Second Stage: Exploration
Notes: In the first stage, an introduction is made with one of the several first-contact mechanisms such as QR codes, mDNS, and DIDs.

## Slide 37
First Stage: Introduction
QR Codes
mDNS
And more
DIDs
Second Stage: Exploration
Notes: After the introduction, WoT Discovery defines a set of second-stage "exploration" mechanisms that provide actual access to metadata.
This can be done in 2 ways: a single TD can be retrieved or a link for TD directories becomes available.

## Slide 38
First Stage: Introduction
QR Codes
mDNS
And more
DIDs
Second Stage: Exploration
Notes: After the introduction, WoT Discovery defines a set of second-stage "exploration" mechanisms that provide actual access to metadata.
This can be done in 2 ways: a single TD can be retrieved or a link for TD directories becomes available.

## Slide 39
First Stage: Introduction
QR Codes
mDNS
And more
DIDs
Second Stage: Exploration
Notes: After the introduction, WoT Discovery defines a set of second-stage "exploration" mechanisms that provide actual access to metadata.
This can be done in 2 ways: a single TD can be retrieved or a link for TD directories becomes available.

## Slide 40
Notes: After the introduction, WoT Discovery defines a set of second-stage "exploration" mechanisms that provide actual access to metadata.
This can be done in 2 ways: a single TD can be retrieved or a link for TD directories becomes available.

## Slide 41
Notes: It is a database with a REST API to access TDs.

## Slide 42
TD
Directory
Register
Update
Retrieve
Search
Notes: The Thing Description Directory service provides mechanisms to register and retrieve WoT metadata and TDs after authentication and authorization.

## Slide 43
Introduction
Exploration
Direct
DNS-based Service Discovery
CoRE link Format
Well-known URIs
TD Server
TD
Directory
Notes: Thus we can summarize the Discovery mechanism like this.

## Slide 44
z
WoT
Thing Description
WoT
Discovery
WoT Binding
Templates
WoT Scripting API
Notes: The WoT Scripting API is an optional building block that lets developers build applications using reusable scripts.

## Slide 45
Notes: It provides a simple and consistent way to interact with Things described by TDs — such as reading properties, invoking actions, and subscribing to events.

## Slide 46
Notes: It makes it easier to develop IoT applications by providing an ECMA Script-based API similar to the Web browser APIs.

## Slide 47
WoT runtime
setInterval(async ()=>){
const tempReading = await thing.readProperty(“position”)
const tempVal = await tempReading.value();
if(tempVal == “open”){
await thing.invokeAction(“closeGrip”)
}
}
Protocol in TD:
HTTP
Modbus
Notes: Once you have a TD, you can use the API to build dashboards or automate device logic without worrying about the underlying protocols.

## Slide 48
z
WoT
Thing Description
WoT
Discovery
WoT Binding
Templates
WoT Profile
WoT Scripting API
Notes: By design, TDs are flexible and able to describe anything without any limitations.

## Slide 49
z
WoT
Thing Description
WoT
Discovery
WoT Binding
Templates
WoT Profile
Notes: By nature, TD is flexible and able to describe anything without any limitations.

## Slide 50
Notes: However, in some cases, depending on the Thing’s purpose, it may be a good idea to limit the TD to prevent unnecessary implementation load.

## Slide 51
Notes: In some cases, depending on the Thing’s purpose, it may be a good idea to limit the TD to prevent unnecessary implementation load.

## Slide 52
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 53
Connect
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 54
Connect
Implementation
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 55
Connect
Implementation
Reduced implementation effort
Notes: However, in some cases, depending on the Thing’s purpose, it may be a good idea to limit the TD to prevent unnecessary implementation load.

## Slide 56
Connect
Configurations
Network Protocol:
Security:
Data Structure:
Notes: However, in some cases let's say you are trying to communicate with your smart bulb with your smartphone, the lack of limitation of the TDs causes an unnecessary implementation load to communicate with every Thing.

## Slide 57
Connect
Configurations
Network Protocol:
Security:
Data Structure:
HTTP
MQTT
CoAP
Notes: and while implementing a thing profile makes it way easier with providing guidance. For instance, developers don’t have to think about which protocols to choose.

## Slide 58
Connect
Security Key:
Configurations
IP Address:
***********
192.168. 0.1
A Specific Profile
Notes: Thus, in those cases, Profile limits the capabilities of the TDs which enables out of box interoperability among things and devices. And make it possible to communicate with only minor configuration operations such as entering a key or IP address.

## Slide 59
Scripting runtime system
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 60
Scripting runtime system
WoT runtime
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 61
WoT runtime
Scripting runtime system
WoT Scripting API
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 62
WoT runtime
Scripting runtime system
WoT Scripting API
Portable application
scripts
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 63
WoT runtime
Portable application
scripts
Behavior of
Things,
Consumer,
Intermediaries.
Notes: This is achieved by integrating a scripting runtime system into the WoT Runtime, where the WoT Scripting API enables the use of portable application scripts that define the behavior of Things, Consumers, and Intermediaries.

## Slide 64
WoT runtime
setInterval(async ()=>){
const tempReading = await .readProperty("temperature")
const tempVal = await tempReading.value();
if(tempVal < 25){
await .invokeAction("increaseTemperature")
}
}
Protocol in TD: HTTP
httpThing
httpThing
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 65
WoT runtime
setInterval(async ()=>){
const tempReading = await .readProperty("temperature")
const tempVal = await tempReading.value();
if(tempVal < 25){
await .invokeAction("increaseTemperature")
}
}
Protocol in TD: Modbus
modbusThing
modbusThing
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 66
WoT runtime
setInterval(async ()=>){
const tempReading = await thing.readProperty(“temperature”)
const tempVal = await tempReading.value();
if(tempVal < 25){
await thing.invokeAction(“increaseTemperature”)
}
}
Protocol Option:
HTTP
Modbus
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 67
WoT runtime
setInterval(async ()=>){
const tempReading = await thing.readProperty(“temperature”)
const tempVal = await tempReading.value();
if(tempVal < 25){
await thing.invokeAction(“increaseTemperature”)
}
}
Protocol Option:
HTTP
Modbus
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 68
Application Logic does not Change!
Notes: We will focus on consumers. The development phase becomes easier with functions like read property and invoke action. Since you don’t have to decide on the protocols when programming controllers. It turns abstract run time scripts into concrete protocol messages.

## Slide 69
Connect
Notes: Thus, in those cases, Profile limits the capabilities of the TDs which enables out of box interoperability among things and devices. And make it possible to communicate with only minor configuration operations such as entering a key or IP address.

## Slide 70
Key:
IP Address:
***********
192.168. 0.1
Configurations
Notes: Thus, in those cases, Profile limits the capabilities of the TDs which enables out of box interoperability among things and devices. And make it possible to communicate with only minor configuration operations such as entering key or IP address.

## Slide 71
Key:
IP Address:
***********
192.168. 0.1
Configurations
Notes: Thus, in those cases, Profile limits the capabilities of the TDs which enables out of box interoperability among things and devices. And make it possible to communicate with only minor configuration operations such as entering key or IP address.

## Slide 72
Productivity
Integration cost
Notes: To summarize, WoT enables implementing device logic by reusable scripts executed in a runtime system for IoT applications which aims to improve productivity and reduce integration costs.

## Slide 73
NEXT VIDEO
Architecture
Patterns
Building
Blocks
Thing
Description
Notes: Next video we will explain the Thing Description.

## Slide 74
NEXT VIDEO
Architecture
Patterns
Building
Blocks
Thing
Description
Notes: Next video we will explain the Thing Description.

## Slide 76
Next Video
Subscribe to our Channel
Playlist